## Slide 1
PRESENTED BY : ZUBAIR MAQBOOL
ENROLL : 4663
B.E : 7th
SECTION : B

## Slide 2
CONTENTS
INTRODUCTION
COMPONENTS OF PASSIVE SOLAR BUILDINGS
DESIGN PRINCIPLES OF PASSIVE SOLAR BUILDINGS
METHODS OF DESIGN
CONCLUSION

## Slide 3
INTRODUCTION
Solar building refers to use of sun light to heat and cool the living space of the building
TYPES OF SOLAR BUILDING
Active solar building
  These buildings use mechanical devices such as pumps and fans to move the heat.
  Photo voltaic panels are used to collect solar energy
Passive solar building
  No mechanical devices are used in this building
  It takes advantage of local breezes and landscape features
  Simple system is used to collect and store sun energy

## Slide 4
COMPONENTS OF PASSIVE SOLAR BUILDINGS
COLLECTION
  it includes windows and skylights
  its purpose is to allow sunlight into building to heat the space and storage mass
STORAGE
  It stores collected solar heat
  In most cases heat is collected in daytime & used at night
  Storage subsystem includes parts of floor & interior walls of building
DISTRIBUTION
  This system is accomplished by arranging the functional spaces of building
  Distribution of heat takes place by combination of radiation and convection
4. CONTROL
  A balance between size ;shape and location of sub system is achieved to ensure better performance of buildings.

## Slide 5: DESIGN PRINCIPLES OF PASSIVE SOLAR BUILDING
1.ORIENTATION
  These buildings must be faced towards south direction
  Longer side is oriented along east-west direction
  No evergreen trees along face
2 OVERHANGS AND SHADING
  These are used to let sunlight fall on glass during winter and to keep it off the glass in summer

## Slide 6
3.THERMAL MASS
It is a solid or liquid material that will absorb and store heat until it is needed

## Slide 7
METHODS OF DESIGN
DIRECT GAIN METHOD
  Actual living space acts as collector, absorber and distribution system
    In this method 60 to 75% of solar energy striking the windows is utilized

## Slide 8
RULES OF DIRECT GAIN METHOD
Thickness of thermal mass should be less than 6 inches
Thermal mass should not be covered with wall to wall carpeting
Use medium colour for masonry floor and light colour for walls
For every sq. feet of glass use 150 pounds of masonry
There should be no cavities in concrete block used as thermal mass
Surface area of thermal mass exposed to sunlight should be 9 times the area of glass

## Slide 9
INDIRECT GAIN SYSTEM
Thermal mass is kept between glass and living space
This method will utilize 30 to 45% of sun energy striking the glass

## Slide 10
Rules of indirect gain system
Exterior of thermal mass should be dark
Take a minimum space of 4 inches between glass and mass
Thermal mass should be 10-14 inches for bricks and 12-18 inches for concrete

## Slide 11
Conclusion
Passive solar buildings are the part of green buildings by these buildings we are able to use solar energy and non renewable sources can be saved to large extent
It also reduces the cost of electric billing

## Slide 12
Thank you